## Slide 1: Occupational Exposure to Formaldehyde

## Slide 2: Uses of Formaldehyde
Preservative in medical laboratories
Embalming agent in mortuaries
Manufacture of urea, phenol, and melamine resins and for a variety of special industrial chemicals
Adhesives in the manufacture of particle board, fiberboard, and plywood, and for molding, paper treating and coating, textile treating, surface coating, and foams for insulation
Formaldehyde is also used as a treatment for athlete's foot, in cough drops, skin disinfectants, mouthwashes, spermatic creams, as a disinfectant for vasectomies and root canals

## Slide 3: Chemical Description
Chemical formula: HCHO
Colorless gas with a pungent, suffocating odor
Synonyms
–Gaseous formaldehyde are methanal, methyl aldehyde, and methylene oxide
–Aqueous solution is formalin
Highly flammable gas or a combustible liquid
–Vapors may travel to a source of ignition and flash back
–Poisonous gases are produced if it catches on fire
–Containers of formaldehyde may explode in fire

## Slide 4: Routes of Exposure
In clinical and laboratory settings, exposure to formaldehyde typically occurs through inhalation and skin exposure
–Inhalation occurs when containers are left uncapped, heated or instruments are not properly vented
–Formaldehyde should be used in a chemical fume hood
Skin exposure occurs when formaldehyde is in contact with skin or eyes. Proper personal protective equipment (see notes) should be worn to minimize the amount of skin contact
Notes: Recommended Personal Protective Equipment: Ensure that workers use PPE such as impervious clothing, gloves, aprons, safety glasses and/or chemical splash goggles to prevent skin and eye contact with formaldehyde. Where exposure assessment shows levels at or above the OSHA action limit, proper engineering controls including the use of respirator will be required. All respiratory protection must be according the OSHA approved respiratory protection program.

## Slide 5: Health Effects
Formaldehyde is a potential human carcinogen.
Airborne concentrations above 0.1 ppm (parts per million parts of air) can cause irritation of the eyes, nose, and throat.
Excessive inhalation of vapors can cause acute respiratory distress, chemical pneumonitis, and bronchial asthma .
Skin contact may cause various skin reactions including irritation and sensitization.
–Sensitizer: A chemical that causes a substantial proportion of exposed people or animals to develop an allergic reaction in normal tissue after repeated exposure to the chemical.

## Slide 6: Health Effects
Acute: Eye and respiratory irritation can result from exposure to the liquid and vapor forms. Severe abdominal pains, nausea, vomiting and possible loss of consciousness could occur if ingested in large amounts.
Chronic: High concentration of vapor inhaled for long periods can cause laryngitis, bronchitis or bronchial pneumonia. Prolonged exposure may cause conjunctivitis. Nasal tumors have been reported in animals.
Know the health effects and if you experience any, report them to your supervisor immediately!

## Slide 7: How EH&S Monitors Exposure
Passive monitors, produced as badges are among the new technologies for detecting formaldehyde. For example, the Assay Technology ChemDisk monitor, shown in the photo, is worn on the lapel to represent the breathing zone.
Monitor is worn for at least 15 minutes
or the duration of the work procedure.
The monitor is collected and sent to an AIHA accredited laboratory for testing.
A report of the results is distributed to the supervisor and the employee.
Passive monitor to determine airborne exposure.

## Slide 8: Exposure Assessment
EH&S conducts formaldehyde assessment when it determines that employees are or may be potentially exposed.
When does EH&S perform air monitoring?
–As part of its initial assessment, EH&S may conduct air monitoring to determine baseline with current use and controls.
–Periodic monitoring are performed when initial results are above the limits or there is a change in the procedure.
Air monitoring results are compared to OSHA and ACGIH limits.

## Slide 9: Employee Exposure Limits for Formaldehyde
OSHA
–Action Level (AL), 0.5 ppm measured over 8 hours
–Permissible exposure limit (PEL) 0.75 ppm measured as an 8-hour time weighted average (TWA)
–Short Term Exposure Limit (STEL) is 2 ppm, maximum exposure allowed during a 15-minute period
–If exposure exceeds any of these limits, changes must be made to reduce employee exposure.
ACGIH TLV
– Ceiling 0.3 ppm, instantaneous measurement if possible

## Slide 10: Labeling and Storage
Label must include:
–Chemical name without abbreviations or symbols
–Name of the responsible party
–Hazard class
–Date opened or expiration date recommended
All mixtures and solutions, composed of 0.1 percent or greater formaldehyde and all materials capable of releasing formaldehyde in excess of 0.1 ppm must include a warning that formaldehyde presents a potential cancer hazard
Store in a secure, closed container below shoulder level in secondary containment with Class 9 carcinogens

## Slide 11: Required Training
Initial Training
–Completion of this presentation and passing grade on quiz
–Specific training from supervisor on the safe use of formaldehyde in your work environment
Annual training for all employees exposed to formaldehyde concentrations of 0.1 ppm or greater
  ECU employees are generally not exposed to concentrations this high

## Slide 12: Safe use in Clinic or Laboratory
Create a lab safety plan for formaldehyde use
Model plan available
SDS available
Know the signs and symptoms of exposure
Use only in areas designated for carcinogens
Wear the appropriate personal protective equipment
–Front or back closing lab coat
–Safety goggles
–Nitrile or neoprene gloves (Latex gloves do not provide any chemical resistance)
–No shorts or open toed shoes
Wash hands, counters and equipment after use

## Slide 13: Spills and Leaks
Wear suitable personal protective equipment.
Do not touch the spilled material; stop the leak if it is possible to do so without risk.
Remove sources of ignition.
Isolate the area so others do not inadvertently become exposed or transport the spilled material.
If you cannot safely handle the spill, contact EH&S immediately at 328-6166.

## Slide 14: Questions
211 South Jarvis Street, Suite 102, Greenville NC 27858
Online: www.ecu.edu/oehs
Email: safety@ecu.edu
Phone: (252) 328-6166
QUIZ
To receive credit for this training please complete the linked