## Slide 1: Occupational Noise Exposure
Hearing Conservation Training Program
Presented by
ECU Office of Environmental Health and Safety

## Slide 2: Did You Know?
About 30 million workers are exposed to hazardous noise on the job
Noise-induced hearing loss is the most common occupational hazard for American workers
Hearing loss from noise is slow and painless; you can have a disability before you notice it
If you must raise your voice to speak with someone only 3 feet away, you are in high (hazardous) noise.
It is 100% preventable
Noise and Hearing Loss Prevention | NIOSH | CDC.
Source

## Slide 3: What is Noise?
Noise is any unwanted sound
By-product of many industrial processes, e.g. operating machinery
Exposure to high levels of noise may lead to hearing loss and other harmful health effects

## Slide 4
General
Estimate of
Work-Related
Noises
Source: NIOSH

## Slide 5: Common Sounds may be louder than you think …

## Slide 6: Anatomy of the Ear
Region where damage that causes hearing loss occurs
Containing the vestibule, semicircular canals, and the cochlea.

## Slide 7: Signs of Hearing Loss
Do you ask people to speak louder so that you can hear?
Do you have to turn the TV or Radio so loud that others complain?

## Slide 8: Hearing Loss
Temporary Hearing Loss
  results from short term exposure to noise
  hearing returns when away from the noise
Permanent Hearing Loss
- results from exposure to a moderate or high level of noise over a long period of time
-hearing loss is PERMANENT
Notes: Employers must provide hearing protectors to all workers exposed to 8-hour TWA noise levels of 85 dB or above. This requirement ensures that employees have access to protectors before they experience any hearing loss. Employees must wear hearing protectors:For any period exceeding 6 months from the time they are first exposed to 8-hour TWA noise levels of 85 dB or above, until they receive their baseline audiograms if these tests are delayed due to mobile test van scheduling;
If they have incurred standard threshold shifts that demonstrate they are susceptible to noise; and
If they are exposed to noise over the permissible exposure limit of 90 dB over an 8-hour TWA.

## Slide 9: Selection of Hearing Protection Devices
Hearing protection devices are selected according to:
  Employee comfort
  Level of noise exposure
  NRR of device
  Type of work being performed
  Environmental conditions
  Employee may select hearing protection from a variety of suitable hearing protectors provided by employer.

## Slide 10: Types of Hearing Protection Devices
Ear muffs
Foam insert earplugs
Semi-aural earplugs
Earmuffs
Earplugs
Ear caps or bands

## Slide 11: Ear Muffs
Advantages
More protection at higher frequencies than earplugs
Various NRRs available
Durable, long lasting
Can be fitted on hard hat
Reusable
Disadvantages
Higher cost
Eye glasses can interfere with ear muff seal
May be uncomfortable in hot environments
Must be cleaned before use by another worker

## Slide 12: Foam Insert Earplugs
Advantages
More protection at lower frequencies than muffs
Various NRRs available
Inexpensive; disposable
Can be custom molded for individual worker
Reusable plugs are available
Disadvantages
Hands must be cleaned before inserting earplugs
Improper insertion reduces NRR value

## Slide 13: Semi-aural Caps
Advantages
Various NRRs available
Easy to insert
May be used several times
Ideal for people going in and out of noisy areas
Disadvantages
Improper insertion reduces effectiveness
More expensive than ear plugs
Typically have lower NRRs than plugs or muffs

## Slide 14: Fit, Use and Care of Hearing Protection Devices
Employer must ensure proper initial fitting
Employer must supervise the correct use of hearing protectors
Hearing protectors must be replaced as necessary at no cost to employee, contact your supervisor
Hearing protection devices must be cleaned and stored according to the manufacturer’s specification\
For questions concerning selection of hearing protection based on NRR and proper fit contact EH&S @ 328-6166

## Slide 15: Audiometric Testing
Monitors employee’s hearing over time
Baseline audiogram must be performed within first 6 months of work exposure ( 8 hour TWA ≥ 85 dBA)
Annual audiograms are required each year after baseline audiogram
Employer must pay for the cost of each required audiogram
Notes: Employers must provide baseline audiograms within 6 months of an employee's first exposure at or above an 8-hour TWA of 85 dB. It is important to test workers' hearing annually to identify deterioration in their hearing ability as early as possible. This is to ensure a quick followup measures before hearing loss progresses. Employers must compare annual audiograms to baseline audiograms to determine whether the audiogram is valid and whether the employee has lost hearing ability or experienced a standard threshold shift (STS). An STS is an average shift in either ear of 10 dB or more at 2,000, 3,000, and 4,000 hertz.

## Slide 16: Why Do Audiometric Testing?
Obtain a Baseline Audiogram for future comparison
Identify occupational hearing loss
Identify Standard Threshold Shifts (STS)
An STS is an average shift in either ear of 10 dB or more at 2,000, 3,000, and 4,000 hertz.

## Slide 17: Normal Vs Noise-Induced Audiometric Testing?

## Slide 18: Access to Information and Training Materials
A copy of the OSHA 29 CFR1910.95 standard available to affected employees online @ www.osha.gov
OSHA Occupational noise exposure standard must be posted in the workplace
Employer is responsible for record keeping regarding employee noise exposure measurements for 2 years. However, the audiometric test records are kept for the duration of employment of the employees who are in the hearing conservation program.

## Slide 20: Questions
211 South Jarvis Street, Suite 102, Greenville NC 27858
Online: www.ecu.edu/oehs
Email: safety@ecu.edu
Phone: (252) 328-6166
QUIZ
To receive credit for this training please complete the linked