## Slide 1
Occupational
Heat Stress
Presented by
ECU Office of Environmental Health and Safety

## Slide 2: Individuals At Risk
All individuals who work in hot environments (inside and outside) are at risk of developing heat stress.
More intense and strenuous workloads, put individuals at a greater risk.
Wearing PPE such as respirators and protective suits can also increase this risk.

## Slide 3: Contributing Factors
Environmental Factors
  Temperature
  Humidity
  Radiant Heat
  Air Velocity
Temperature is not the only indicator!!

## Slide 4: Contributing Factors
Personal Factors
    Age
    Weight
    Fitness
    Acclimatization – increased tolerance to heat that comes from working in a hot environment for a period 1-2 weeks.

## Slide 5: The Body’s Response to Heat
Increased Blood Circulation
  Blood is circulated to the skin which increases skin temperature and allows the body to give off excess heat through the skin.
  This is why your face turns red when you are hot.
  However, physical labor requires blood to fuel the muscles; therefore, less blood is available to flow to the skin surface and because of this, less heat is released from the body.

## Slide 6: The Body’s Response to Heat
Sweating
  Sweating is an effective way to cool the body when humidity is relatively low.
  Sweating is most effective when the sweat evaporates from the skin rather than drips off or is wiped off.
  A young male can sweat as much as one quart per hour. (2-3 gallons per day)

## Slide 7: Heat Disorders
Heat Rash
Heat Cramps
Heat Exhaustion
Heat Stroke

## Slide 8: Heat Disorders
Heat Rash
  Also known as “Prickly Heat.”
  Occurs when sweat cannot freely evaporate from the skin and sweat ducts become plugged. This inflammation can cause a red rash.
  Can be prevented by wearing clothes that allow sweat to evaporate as well as bathing regularly and drying the skin.

## Slide 9: Heat Disorders
  Heat Cramps
  Cramps in the arms, legs or abdomen
  Occur in individuals who sweat profusely then drink large quantities of water, but do not adequately replace the body’s salt loss.
  To prevent, ensure that salts are replaced during and after heavy sweating.

## Slide 10: Heat Disorders
Heat Exhaustion
Mild form of shock caused when the circulatory system begins to fail as a result of the body’s inadequate effort to give off excessive heat.
Although not an immediate threat to life, if not properly treated, could evolve into heat stroke.

## Slide 11: Heat Disorders
Heat Exhaustion - Symptoms
Skin is clammy and moist
  Extreme weakness or fatigue
  Nausea
  Headache
  Complexion pale or flushed
  Body temperature normal or slightly elevated

## Slide 12: Heat Disorders
Heat Exhaustion - Treatment
  Do not leave the person alone
  Move to a cool place to rest
  Drink water or electrolyte fluids
  Treat for shock, if necessary
  If unconscious, fails to recover rapidly, has other injuries, or has a history of medical problems, seek medical attention.

## Slide 13: Heat Disorders
Heat Stroke
Severe and sometimes fatal condition resulting from the failure of the body to regulate its core temperature.
The body’s normal cooling mechanisms stop functioning, sweating stops.
True medical emergency requiring immediate medical attention.

## Slide 14: Heat Disorders
Heat Stroke - Symptoms
  Stop Sweating
  Rapid Pulse
  Mental Confusion
  Loss of Consciousness
  Convulsions
  Body Temperature > 105
  Hot, dry skin
  Can die unless treated promptly

## Slide 15: Heat Disorders
Heat Stroke - Treatment
  Call 911
  Remove victim to a cool area
  Soak clothing with cool water and fan vigorously to increase cooling
  Monitor vital signs

## Slide 16: Prevention Methods
Acclimatization
Work in pairs
Drink plenty of cool water or electrolyte replacement fluids even if not thirsty. (One small cup every 15-20 minutes)
Be able to recognize early signs & symptoms of heat-induced illness and take appropriate action to prevent serious heat disorders.
Schedule most strenuous work during the coolest times of the day.

## Slide 17: Prevention Methods
Spend as little time as possible in direct sunlight.
Take frequent breaks in cool, shaded areas.
Wear light, loose fitting, clothing.
Avoid caffeine, which can make the body lose water.
Rotate workers in and out of hot areas if possible.

## Slide 18: Heat Stress Measurement
Personal Heat Stress Monitor
Area Heat Stress Monitor

## Slide 19: Wet Bulb Globe Temperature Index
WBGT is a number that is calculated as a combination of humidity, radiant, and ambient temperature readings.
This number is then combined with work load to determine heat stress potential.
The following table displays the recommended work/rest regimen for corresponding WBGT values.

## Slide 20: Work/Rest Regimen
 | Work |  |  | Load* |  | 
Work/rest regimen | Light |  | Moderate |  | Heavy | 
Continuous work | 30.0°C | (86°F) | 26.7°C | (80°F) | 25.0°C | (77°F)
75% Work, 25% rest, each hour | 30.6°C | (87°F) | 28.0°C | (82°F) | 25.9°C | (78°F)
50% Work, 50% rest, each hour | 31.4°C | (89°F) | 29.4°C | (85°F) | 27.9°C | (82°F)
25% Work, 75% rest, each hour | 32.2°C | (90°F) | 31.1°C | (88°F) | 30.0°C | (86°F)
*Values are in °C and °F, WBGT. These TLV's are based on the assumption that nearly all acclimatized, fully clothed workers with adequate water and salt intake should be able to function effectively under the given working conditions without exceeding a deep body temperature of 38°C (100.4° F). They are also based on the assumption that the WBGT of the resting place is the same or very close to that of the workplace. Where the WBGT of the work area is different from that of the rest area, a time-weighted average should be used (consult the ACGIH 1992-1993 Threshold Limit Values for Chemical Substances and Physical Agents and Biological Exposure Indices (1992). These TLV's apply to physically fit and acclimatized individuals wearing light summer clothing. If heavier clothing that impedes sweat or has a higher insulation value is required, the permissible heat exposure TLV's in Table III:4- 2 must be reduced by the corrections shown in Table III:4-3. |  |  |  |  |  | 
PERMISSIBLE HEAT EXPOSURE THRESHOLD LIMIT VALUES
Source: ACGIH 1992.

## Slide 21: Heat Stress Monitoring
If you are unsure of the Heat Stress Potential that your employees are exposed to, contact EH&S to conduct Heat Stress Monitoring.

## Slide 22: Questions
211 South Jarvis Street, Suite 102, Greenville NC 27858
Online: www.ecu.edu/oehs
Email: safety@ecu.edu
Phone: (252) 328-6166
QUIZ
To receive credit for this training please complete the linked