## Slide 1: Personal Protective Equipment

## Slide 2: Personal Protective Equipment
Personal Protective Equipment (PPE) is any safety equipment that is worn to prevent injury in the workplace, when engineering and administrative controls are not feasible or are being implemented.
PPE must be provided when necessary by reason of hazards encountered that are capable of causing injury or impairment. They are no substitute for engineering, work practice, and/or administrative controls.
At best, PPE creates a barrier between the hazard and worker contact. They do not eliminate the hazard, so if the equipment fails then exposure occurs. For this reason, they must be worn always to provide protection.

## Slide 3: OSHA PPE Standard
29 CFR 1910.132
The standard requires employers to:
Assess the workplace to determine if hazards are present
Select and provide appropriate PPE that fits each affected employee
Train employees on how to use PPE correctly

## Slide 4: Hazard Assessment
The employer must:
  Evaluate every job function
  Determine if hazards are present
  Check for hazards to all parts of the body
  Determine appropriate PPE
Common hazards include chemical exposures, falling or dropping objects, particulates, temperature extremes, light radiation, moving equipment and parts, sharp objects, etc.
Notes: Written certification of hazard assessment shall identify:
  Workplace evaluated
  Person certifying that the evaluation has been performed
  Date(s) of the hazard assessment
  Identification of document as a certification of hazard assessment

## Slide 5: PPE Selection
Selected PPE shall:
protect each employee from identified hazards
be of safe design and construction
be sanitary and reliable
provide each employee with a good fit
Meets American National Standards Institute (ANSI) standard or other approved standards
Notes: If hazards are present the employer shall:
  Select and have each affected employee use appropriate PPE for identified hazards
  Communicate selection decisions
  Select PPE that fits each employee

## Slide 6: Training Requirements
Employer must train employees in the following areas before issuing them a PPE:
  When PPE is necessary
  What PPE is necessary
  How to properly don, doff, adjust, and wear PPE
  Limitations of the PPE
  Proper care, maintenance, useful life and disposal of the PPE

## Slide 7: Training Requirements Cont’d
Employees must demonstrate an understanding of the training and the ability to use PPE properly before being allowed to perform work requiring the use of PPE
Training should be documented through a written certification to verify that each employee has received and understood the training requirements

## Slide 8: Retraining Requirements
Employees shall be retrained due to:
Changes in the workplace
Changes in types of PPE used
Inadequacies in an affected employee’s knowledge
Assessment that the use of assigned PPE indicate that the employee has not retained training
Or as determined by results of accident investigation

## Slide 9: Routes of Exposure
Inhalation
Skin Absorption
Ingestion
Injection
Knowing the hazards and how to protect yourself is the key to your safety!
Create a barrier using a PPE!

## Slide 10: Types of PPE
Eye & Face Protection
Respiratory Protection
Head Protection
Foot Protection
Hand Protection
Hearing Protection
Body Protection
Fall Protection

## Slide 11
Molten
Metals
Radiation:
Light etc.
Chemicals:
Liquid
Chemicals:
Vapor, gases
Flying
Particles
Heat
Lasers
Heat
Electrical
Work
Must comply with ANSI Z87.1
Eye and Face Protection
Required for exposure to eye and face hazards such as:

## Slide 12: Eye and Face Protection
Employee with prescription lenses are to wear eye protection over prescription lenses without disturbing proper positioning of the prescription or protective lenses
Employee exposed to hazard of radiant energy (light radiation) from welding, cutting must contact EH&S for appropriate level of protection, including shaded filter lenses
All shade numbers for lenses and helmet must conform with OSHA 29CFR1915 and ANZI Z49.1.2005/Z87.1 standards
Important requirements:

## Slide 13
Vapors
Dusts
Fogs
Fumes
Sprays
Gases
Smokes
Mists
Respiratory Protection
Required for protection against hazards such as:
These contaminants can settle anywhere from the inhalable (nose) to respirable (lung) region of the respiratory tract
Respirators must be NIOSH approved

## Slide 14: Respiratory Protection
when engineering controls are not feasible or are being implemented
When exposure levels exceed the permissible exposure limit (PEL)
For maintenance and repair activities that may result in exceeding the PEL
During emergency Response where type and/or concentration of contaminant is unknown
Voluntarily according to the OSHA voluntary protection requirements
See EH&S website for more on respiratory protection program requirements: http://www.ecu.edu/cs-admin/oehs/ih/upload/EH-S-Respiratory-Protection-Program.pdf
Respirators shall only be used:

## Slide 15: Respiratory Protection
When the use of respirators are required, the following elements shall apply:
  Training
  Fit testing
  Medical evaluations
  Care and maintenance
  Procedures for respirator selection
  Procedures for routine & emergency use
  See EH&S website for more on respiratory protection program requirements: http://www.ecu.edu/cs-admin/oehs/ih/upload/EH-S-Respiratory-Protection-Program.pdf on respiratory protection program requirements

## Slide 16: Head Protection
Required when employees are in areas where there is a potential for injury to the head from:
  Falling objects
  Flying objects
  Fixed object
  Protruding material
  High voltage equipment and work involving

## Slide 17: Types of Head Protection
Type 2
Class G
Type 1
reduce force of impact from a blow to the top of the head
Tested to withstand 2200 volts
provide protection against both side impact (lateral) and blows to the top of the head
Class E
Class C
Tested to withstand 20,000 volts
No electrical protection
Must comply with ANSI Z89
  Note: Before each use, inspect for signs of dents, cracks, penetration, and any damage due to impact, rough treatment or wear

## Slide 18: Foot Protection
Required when employees are in areas where there is danger of foot injury due to
falling and rolling objects
slip hazards or objects piercing the sole, and
where employees are exposed to electrical hazards
Must comply with ASTM F2413 – 05

## Slide 19: Potential Hazards
Impact Injuries Spills & Splashes Compression Injuries
Electrical Shocks Slipping Heat/Cold

## Slide 20: Selection, Care and Maintenance
Slip resistant soles
Oil resistant soles
Protect against punctures and penetration
Compatible with environment
Assure proper fit
Protect toes against impact and compression
Conductive protection (minimize static electricity)
Be inspected for cuts, tears, cracks, worn soles and other damage
Be cared for according to manufacturer’s recommendations

## Slide 21: Hand Protection
Skin absorption of harmful substances
Severe cuts or lacerations
Severe abrasions
Punctures
Chemical burns
Thermal burns
Harmful temperature extremes
Protection must be compatible with hazard!
Required when employees’ hands are exposed to hazards such as

## Slide 22: Glove Selection
Glove selection depends on type of hazard
Check SDS for guidelines for chemical hazards
Choose compatible material as no one material is suited for all chemicals
Consult the manufacturer’s chemical resistance guide
Latex may cause sensitivity or become an allergen to those exposed. If latex gloves must be used, choose reduced-protein, powder-free latex gloves.
Powered gloves must not be used for medical/clinical purposes per FDA ban
Always consider chemical (or other substance) to be used, dexterity needed, extent of protection and type of work when selecting gloves

## Slide 23
guard against injuries from sparks or scraping against rough surfaces
protects and insulate against heat or cold
nitrile, vinyl, neoprene, etc. protect against chemical exposure
against cuts and scratches; used commonly with sharp instruments
insulate hands from intense heat; commonly used with molten materials
protects against mild irritants
Fabric Gloves
Leather Gloves
Chemical Resistant Gloves
Metal Mesh Gloves
Aluminized Fabric Gloves
Disposable Gloves
Common Types of Gloves

## Slide 24: Glove Donning and Doffing
Source: NIOSH

## Slide 25: Hearing Protection
Noise is an unwanted sound. Hearing protection is required when exposure to noise level is at or above the OSHA action level of 85dBA.
Hearing loss occurs as a result of damage to the delicate structures (sensory cells) of the ear – this happens without employee’s notice.
Region where damage that causes hearing loss occurs

## Slide 26: Types of Hearing Protection
There are three types of hearing protection:
Earmuffs
Earplugs
Ear caps or bands

## Slide 27: Donning Hearing Plugs
Roll the earplug up into a small, thin “snake” with your fingers. You can use one or both hands
Pull the top of your ear up and back with your opposite hand to straighten out your ear canal. The rolled-up earplug should slide right in
Hold the earplug in with your finger. Count to 20 or 30 out loud while waiting for the plug to expand and fill the ear canal. Your voice will sound muffled when the plug has made a good seal
Source: NIOSH

## Slide 28: Body Protection
The skin (covering the body) is the largest organ of the body, which also exposes it easily to occupational hazards. Body parts such as chest, torso, back, arm, legs must be protected from hazards such as:
  Intense heat
  Cuts
  Hazardous chemicals
  Splashes from hot metals and other liquids
  Contact with potentially infectious materials, like blood
  Radiation
  Impacts from tools, machinery and materials etc.

## Slide 29: Types of Body Protection
There are different types of body protective clothing which includes:
Coveralls
Full body suits
Sleeves
Apron
Coats including – including lab coats, insulated coats and other design

## Slide 30: Body Protection
Select and use the right type of protective clothing for the right job
Protective clothing must fit and be used properly, else they will become a hazard to user
Inspect protective clothing before use
Store in clean, cool, dry and ventilated area
Safe Practice:

## Slide 31: Body Protection
Protective Clothing Materials

## Slide 32: Fall Protection
  Required when risk of falling at heights of 6 feet or greater when area is not guarded or protected by other fall protection measures
  Work at any height in aerial lifts, powered platforms and similar equipment
  Include safety belts, lifelines, lanyards
Photo: ASSE

## Slide 33: Care of PPE
Always check PPE for damage before and after use
Clean PPE before storing
Dispose of and replace damaged PPE
Properly store PPE and avoid conditions that could damage them, such as heat, light, moisture, etc.
Do not fix or repair a damaged PPE

## Slide 34: PPE Acquisition and Replacement
PPE is provided by Supervisor/department concern- not the employee
If performing activity and you do not have PPE, contact Supervisor for PPE prior to starting activity
Employee may be responsible for lost or damaged PPE
State Equipment Use Policy must be strictly complied with

## Slide 35: Responsibilities

## Slide 36: Questions
211 South Jarvis Street, Suite 102, Greenville NC 27858
Online: www.ecu.edu/oehs
Email: safety@ecu.edu
Phone: (252) 328-6166
QUIZ