Laboratory Inspections

| Weekly Inspection List | Yes | No | Correction Date |
| --- | --- | --- | --- |
| All lights, including exit lights, are in working condition. |  |  |  |
| Aisles and exits are clear of all obstructions. |  |  |  |
| Eyewash station is clear from obstructions. |  |  |  |
| Eyewash station has been cleaned and run for at least 30 seconds. If not properly functioning, tag “Out of Service” and place immediate priority work order for repair. |  |  |  |
| No stored items are placed within 18 inches of a sprinkler head or ceiling. |  |  |  |
| All supplies and moveable equipment stored off the floor. |  |  |  |
| Work areas are free of debris and lab equipment and furnishings are in good condition. |  |  |  |
| Hand washing sink is clean, supplied with soap and towels. |  |  |  |
| Caps are secure on all containers, including waste collection containers. |  |  |  |
| All containers, including temporary secondary containers and hazardous waste containers are properly labeled and in good condition. Waste containers have a completed EH&S waste tag attached. |  |  |  |
| EH&S is contacted when hazardous waste containers are ¾ full and/or prior to 1 year old. |  |  |  |
| Hazardous chemical waste is inspected to insure that the containers are compatible with the waste and free from leaks. |  |  |  |
| Gas cylinders are properly labeled, chained, leak free and capped if not in use. |  |  |  |
| Fume hood/laminar flow hood is clear of stored items and is operating normally (visual indication of flow, sound is normal, no odors). |  |  |  |
| No food, tobacco, gum or cosmetic products are in use or stored in the lab. |  |  |  |
| All lab occupants are wearing fully enclosed shoes and long pants. Safety glasses, lab coats, gloves and other protective equipment is available, clean and in use. |  |  |  |
| Signature of Inspector | Date |

| Weekly Inspection List | Yes | No | Correction Date |
| --- | --- | --- | --- |
| All lights, including exit lights, are in working condition. |  |  |  |
| Aisles and exits are clear of all obstructions. |  |  |  |
| Eyewash station is clear from obstructions. |  |  |  |
| Eyewash station has been cleaned and run for at least 30 seconds. If not properly functioning, tag “Out of Service” and place immediate priority work order for repair. |  |  |  |
| No stored items are placed within 18 inches of a sprinkler head or ceiling. |  |  |  |
| All supplies and moveable equipment stored off the floor. |  |  |  |
| Work areas are free of debris and lab equipment and furnishings are in good condition. |  |  |  |
| Hand washing sink is clean, supplied with soap and towels. |  |  |  |
| Caps are secure on all containers, including waste collection containers. |  |  |  |
| All containers, including temporary secondary containers and hazardous waste containers are properly labeled and in good condition. Waste containers have a completed EH&S waste tag attached. |  |  |  |
| EH&S is contacted when hazardous waste containers are ¾ full and/or prior to 1 year old. |  |  |  |
| Hazardous chemical waste is inspected to insure that the containers are compatible with the waste and free from leaks. |  |  |  |
| Gas cylinders are properly labeled, chained, leak free and capped if not in use. |  |  |  |
| Fume hood/laminar flow hood is clear of stored items and is operating normally (visual indication of flow, sound is normal, no odors). |  |  |  |
| No food, tobacco, gum or cosmetic products are in use or stored in the lab. |  |  |  |
| All lab occupants are wearing fully enclosed shoes and long pants. Safety glasses, lab coats, gloves and other protective equipment is available, clean and in use. |  |  |  |
| Signature of Inspector | Date |

| Semester Inspection List (3 times each year) | Yes | No | Correction Date |
| --- | --- | --- | --- |
| Weekly self-inspection checklists have been completed, signed and are on file. |  |  |  |
| Inventory of hazardous materials is current. |  |  |  |
| A Safety Data Sheet (SDS) is on file for all materials on the inventory and accessible at all times. |  |  |  |
| Updated door posting is posted on laboratory door. |  |  |  |
| Emergency phone numbers are posted near the phone. |  |  |  |
| Emergency action plan has been completed (Including exit path, emergency shut down procedures, meeting location and alarm pull station location.) |  |  |  |
| Chemical Hygiene Plan is available to lab users at all times. |  |  |  |
| Fume hood certification sticker is current. |  |  |  |
| Laboratory ceilings, floors, ventilation ducts and walls are free from damage. |  |  |  |
| All chemical containers in the lab are properly labeled. |  |  |  |
| Extension cords are not used in place of permanent wiring. |  |  |  |
| Electrical cords are protected from physical and chemical damage. |  |  |  |
| Excess chemicals, hazardous waste and expired chemicals have been properly disposed. |  |  |  |
| Corrosives are stored below eye level. (no more than 4-4.5 feet from ground). |  |  |  |
| Chemicals and hazardous wastes are stored inside of secondary containment. |  |  |  |
| Flammable/combustible liquids are stored in a flammable storage cabinet or the total volume of flammables stored in the lab is less than 10 gallons. |  |  |  |
| Refrigerators used to house flammable liquids are approved for such use. |  |  |  |
| Signature of Inspector | Date |

| Semester Inspection List (3 times each year) | Yes | No | Correction Date |
| --- | --- | --- | --- |
| Weekly self-inspection checklists have been completed, signed and are on file. |  |  |  |
| Inventory of hazardous materials is current. |  |  |  |
| A Safety Data Sheet (SDS) is on file for all materials on the inventory and accessible at all times. |  |  |  |
| Updated door posting is posted on laboratory door. |  |  |  |
| Emergency phone numbers are posted near the phone. |  |  |  |
| Emergency action plan has been completed (Including exit path, emergency shut down procedures, meeting location and alarm pull station location.) |  |  |  |
| Chemical Hygiene Plan is available to lab users at all times. |  |  |  |
| Fume hood certification sticker is current. |  |  |  |
| Laboratory ceilings, floors, ventilation ducts and walls are free from damage. |  |  |  |
| All chemical containers in the lab are properly labeled. |  |  |  |
| Extension cords are not used in place of permanent wiring. |  |  |  |
| Electrical cords are protected from physical and chemical damage. |  |  |  |
| Excess chemicals, hazardous waste and expired chemicals have been properly disposed. |  |  |  |
| Corrosives are stored below eye level. (no more than 4-4.5 feet from ground). |  |  |  |
| Chemicals and hazardous wastes are stored inside of secondary containment. |  |  |  |
| Flammable/combustible liquids are stored in a flammable storage cabinet or the total volume of flammables stored in the lab is less than 10 gallons. |  |  |  |
| Refrigerators used to house flammable liquids are approved for such use. |  |  |  |
| Signature of Inspector | Date |

| Annual Inspection List (Complete prior to annual EH&S inspection due in ________) | Yes | No | Correction Date |
| --- | --- | --- | --- |
| Weekly and Semester self-inspection checklists have been completed signed and are on file. All corrections have been completed. |  |  |  |
| Current inventory of hazardous materials is accessible in the lab and forwarded annually to EH&S. |  |  |  |
| An SDS is on file for all materials on the inventory. |  |  |  |
| Current drain disposal log is maintained and forwarded annually to EH&S. (Record all) |  |  |  |
| Chemical Hygiene Plan and Lab Safety Plans have been reviewed with staff. |  |  |  |
| Can each member of the lab staff identify the major chemical hazards, symptoms of exposure and how to recognize a release of the chemical(s)? |  |  |  |
| Has each member of the lab staff completed chemical hygiene/lab safety training? |  |  |  |
| Has each member of the lab staff received lab specific training? |  |  |  |
| Can each member of the lab staff locate all emergency equipment and describe emergency plans? |  |  |  |
| Signature of Inspector | Date |

See the EH&S web site for a printable version of the inspection forms.

*A lab staff member familiar with all operations conducted in the lab should complete forms.

*Completed forms must be retained for use in the annual inspection conducted by University safety personnel.

*Chemical fume hoods are certified at least annually by EH&S.

* Radiation use hoods are certified by the Radiation Safety Officer annually.

*The Biosafety Officer certifies Biosafety cabinets annually.

| Annual Inspection List (Complete prior to annual EH&S inspection due in ________) | Yes | No | Correction Date |
| --- | --- | --- | --- |
| Weekly and Semester self-inspection checklists have been completed signed and are on file. All corrections have been completed. |  |  |  |
| Current inventory of hazardous materials is accessible in the lab and forwarded annually to EH&S. |  |  |  |
| An SDS is on file for all materials on the inventory. |  |  |  |
| Current drain disposal log is maintained and forwarded annually to EH&S. (Record all) |  |  |  |
| Chemical Hygiene Plan and Lab Safety Plans have been reviewed with staff. |  |  |  |
| Can each member of the lab staff identify the major chemical hazards, symptoms of exposure and how to recognize a release of the chemical(s)? |  |  |  |
| Has each member of the lab staff completed chemical hygiene/lab safety training? |  |  |  |
| Has each member of the lab staff received lab specific training? |  |  |  |
| Can each member of the lab staff locate all emergency equipment and describe emergency plans? |  |  |  |
| Signature of Inspector | Date |

See the EH&S web site for a printable version of the inspection forms.

*A lab staff member familiar with all operations conducted in the lab should complete forms.

*Completed forms must be retained for use in the annual inspection conducted by University safety personnel.

*Chemical fume hoods are certified at least annually by EH&S.

* Radiation use hoods are certified by the Radiation Safety Officer annually.

*The Biosafety Officer certifies Biosafety cabinets annually.